## Slide 1
Presented to: ​
Planetary Sciences Advisory Committee
Presented by:​
Dr. Jeffrey Hayes
Discipline Scientist, Science Mission Directorate On Detail to the Space Communications and Navigation (SCaN) organization
Space Operations Mission Directorate
National Aeronautics and Space Administration
November 14, 2023​
Deep Space Network Updates

## Slide 2: Outline
1
2
About SCaN
DSN Status, Challenges, and Plans
2

## Slide 3: Enabling Human Space Exploration and Science
Develop space communication standards as well as positioning, navigation, and timing policies
Manage NASA spectrum; represent NASA on
national and international spectrum management forums
Develop technologies to enable and enhance future mission experience
Develop, operate and manage all NASA space communications capabilities
Represent and negotiate on behalf of NASA on all matters related to space communications and navigation

## Slide 4: Deep Space Network (DSN)
DSN is the only US network dedicated to providing telecommunications services for missions beyond LEO
DSN also supports international spacecraft and scientific investigations (radar, radio astronomy and radio science)
DSN has three complexes, spread across the world to ensure 24/7 coverage
The NASA Jet Propulsion Laboratory (JPL) develops, operates, and manages DSN
DSN’s Role and Structure

## Slide 5
Deep Space Communications are Key to Agency Priorities
Notes: Current and Future projected mission list represents a real challenge
Focus remains on:
Maintaining infrastructure to meet operational needs  “Road to Green”
Adding capacity where budget supports it
Looking for practical ways to improve beyond the higher-cost infrastructure items
Encouraging good stewardship of the assets by the mission community

## Slide 6
  F11
  F12
  F6
  F13
  F7
  F10
  F8
  Near Space Network: Tracking and Data Relay Satellites (TDRS)
NASA Deep Space Network (DSN)
NASA Near Space Network (NSN)
Future Upgrades
Commercial Stations Supporting NSN
Optical
Lunar Exploration Ground Sites (LEGS)
  Canberra, Australia
  Madrid, Spain
  Sardinia, Italy
  Goldstone, California
  Launch Range, Florida
  Blossom Point, Maryland
  Wallops Island, Virginia
  ASF, Alaska
  NOAA, Alaska
  McMurdo, Antarctica
  Guam Remote Ground Terminal
  White Sands Complex, New Mexico
  North Pole, Alaska
  SSC Hawaii
  KSAT
TrollSat, Antarctica
  SSC
  Dongara, Australia
  KSAT
  Singapore
  NSN Station, SSC
  Hartebeesthoek, Africa
  KSAT, Norway
  SSC Kiruna, Sweden
  Hawaii
  - Table Mtn, California
  White Sands, New Mexico
  Ka-band
  Commercial Upgrade Punta Arenas, Chile
  - Ka-band Upgrade Alaska
  DAEP Ka-band Upgrade
  Canberra, Australia
  Ka-band upgrade
  Svalbard, Norway
  - DAEP Ka-band Upgrade
- Ka-band Upgrade
  LEGS 1, White Sands
  LEGS 3, Australia
  LEGS 2, Matjiesfontein,
  South Africa
NASA’s Communications Networks
6

## Slide 7
The DSN Challenge: Rapidly Growing User Needs
7
NASA Office of the Inspector General, 7/12/23
Today
Hours (Per 28-day Interval)
Equivalent Antennas
20,000
18,000
16,000
14,000
12,000
10,000
8,000
6,000
4,000
2,000
0
33.5
29.8
26.0
22.3
18.6
14.9
11.2
7.4
3.7
0.0
2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040
Demand Hours
Excess Demand
Capacity of the DSN
Cadence and complexity of cis-lunar and SMD missions are creating a new level of network demand not seen in decades
  New technologies to achieve Decadal Survey priorities are ever more data hungry
  JWST alone uses 10% of DSN capacity; sending back 25x the data of Hubble
  Infrastructure support has not kept up

## Slide 8: DSN Challenge: Demand Spikes During Artemis
© 2023 California Institute of Technology. Government sponsorship acknowledged.
8

## Slide 9: How SCaN Plans to Support DSN Users
New Deep Space Network (DSN) Capacity & Upgrades
Lunar Exploration Ground Segment (LEGS)
Commercial and International Partners
Optical and other New Technologies
2
3
1
4
Optical will reduce burden on DSN alongside other technologies
Priority 1: Direct-to-Earth assets that meet or exceed LEGS performance
Priority 2: Lunar relay comm and PNT services
Priority 3: Lunar surface comm and PNT capabilities
Further drawing upon commercial service procurement to devlelop lunar relays to reduce user PNT burden and remove DTE line-of-sight constraints (enabling South Pole and Far-Side operations)
Seeking additional commercial and international contributions for both Earth based and Lunar C&N assets
Network of new 18-meter class antennas to support lunar missions
Starting with three government owned, commercial operated sites around the Earth, offering continuous coverage
Commercial LEGS will add additional capacity as demand grows
Building six 34m antennas across all three DSN complexes
Upgrading two DSN antennas at each complex to enable simultaneous operations, enhance uplinks, and increase data rates

## Slide 10: DSN Upgrades: The Road to Green (R2G)
Shaped Surface Sub-reflector
34meter Surface Reflector
Beam Waveguide Shroud
Quadripod
Azimuth Track
Subterranean Pedestal Room
Antenna Spares
Micro
wave Controller
Transmitter
Holography
34 Meter Antenna
Power Plant
Generators
Transformers and Switchgear
R2G examined DSN’s state of health starting in 2020 R2G determined concreate steps to improve network reliability and robustness
Fire Suppression
Operations Center Concept
General Cyber Security
OS Upg
rades
Underground fuel and oil tank (move to above ground)
Water main and sewers
Funds prioritized to address:
Health and safety
IT security
Facility infrastructure
Vulnerable antenna components
Uninterruptible Power Supply

## Slide 11
DAEP is building six 34m Beam Wave Guide (BWG) antennas across all three DSN complexes to provide additional capacity
FY2024 DAEP STATUS SNAPSHOT:
Four 34m BWG deliveries completed (Two in Canberra and two in Madrid)
One 34m BWG in process in Goldstone; Delivery to service April 2026
One 34m BWG in the future at Canberra; Delivery to service expected October 2029
Further expansion after FY30 will be based on a DSN Futures Study, Agency requirements, and available support
May include higher power transmitters, HEF antenna refurbishments, and site diversity measures
Post-FY30 development work is funding dependent
DSN Upgrades: DSN Aperture Enhancement Project (DAEP)
DSS-14
70m
DSS-24
BWG-1
DSS-25
BWG-2
DSS-24
BWG-3
Signal Processing Center SPC-10
DSS-13
R&D
DSS_28
GAVRT
DSS-33
BWG-4
DSS-15
HEF
GDSCC – Goldstone, California
DSS-63
70m
DSS-65
HEF
DSS-54
BWG-1
DSS_55
BWG-2
DSS-56
BWG-3
DSS_53
BWG-4
Signal Processing Center SPC-60
MDSCC – Madrid, Spain
Legend
Decommissioned
Futured DAEP
Delivered DAEP
DSS-43
70m
DSS-34
BWG-1
Signal Processing Center SPC-40
DSS-35
BWG-2
DSS-36
BWG-3
DSS-45
HEF
CDSCC – Canberra, Australia
DSS-33
BWG-4

## Slide 12
Upgrading six DSN antennas (two at each of the three complexes)
Adds capability for near-earth K-band uplink, uplink encoding, and increased data rates (100Mbps+ in Ka)
Provides simultaneous operations across frequency bands – S+Ka-band, X+Ka-band, or simultaneous Ka
Two upgrades completed (Goldstone and Canberra)
Estimated completion dates for additional upgrades:
Goldstone: December 2023
Canberra: July 2024
Spain (DSS-56): April 2025
Spain (DSS-54): March 2028
DSN Upgrades: DSN Lunar Exploration Upgrades (DLEU)

## Slide 13
Lunar Exploration Ground Segment (LEGS)
Representative/ potential commercial locations that may be proposed in response to the NSN procurement to add LEGS capability with S, X, Ka band services
LEGS Site #3: Geraldton, Australia
Government: ASA, ASD
Target Readiness Date: Gateway Launch
Single X/Ka Transmit/Receive Antenna
LEGS Site #2: MTJ, South Africa
Government: SANSA
Target Readiness Date: Gateway Launch
Single X/Ka Transmit/Receive Antenna
LEGS Site #1: White Sands Complex (WSC)
Government: NASA/GSFC
Target Readiness Date: Gateway Launch
Single X/Ka Transmit/Receive Antenna
  LEGS is a new network of DTE antennas that reduce contention for DSN by absorbing new Artemis demands
  LEGS 1 to 3:
    Cover three geographically diverse sites, offering continuous lunar coverage
    18-meter class performance in X and Ka
    Government-owned / contractor operated
  LEGS 4+:
    Locations TBD
    18-meter class performance in X, Ka and S
    Being pursued under full commercial services procurement

## Slide 14
DSN Futures Study
DSN Futures Study objectives:
Look at near-term issues (network scheduling efficiency, network and element brittleness, and fragility), and projected capability needs though 2050
Understand what probable technology will be available, when it could be infused into the DSN, and the required costs
Incorporating SMD (Decadals) and ESDMD (Lunar and Mars architectures) as long-term planning inputs
Study Team members include NASA stakeholders from ESDMD, SMD, and SOMD that are asked to review study progress on a quarterly basis
Plan is to bring the final report to this board for review

## Slide 15
Orchestration of Supply
O&M and sustainment must be orchestrated around mission demands and capability variance is 1:1 with funding variance
Examples only… critical event list is significant
Roman
VIPER
Mars Sample Return
Dragonfly
Veritas

## Slide 16: Synopsis: The Future of SCaN
New Challenges and New Opportunities
    Growing DSN demand is putting flagship SMD and SOMD missions at risk
    Investment in reliability, robustness, and capacity will be necessary to secure DSN’s future
    LEGS government and commercial investments can also offload some Artemis and CLPS requirements from DSN, alongside international partnerships
16

## Slide 17
Acting Deputy Associate Administrator
Space Communications and Navigation (SCaN) Office
Mr. Jeffrey Volosin
Follow us at: https://www.nasa.gov/scan Facebook: NASASCaN Twitter: @NASASCaN